## Slide 1: Classification
Safety of laser products equipment classification and requirements
Class 1 and 1M - laser products that are safe during use, including long-term direct intrabeam viewing
Class 1C - laser products that are intended for direct application of laser radiation for medical procedures
Class 2 and 2M - laser products emit visible radiation that are safe for momentary exposures but are hazardous if staring into the beam

## Slide 2: Classification
Class 3R (Restricted) - laser products that emit radiation that can exceed the maximum permissible exposure (MPE) but the risk of injury in most cases is relatively low. Dazzle, flash-blindness and afterimages may be caused by a beam under low ambient light
Class 3B – laser products that are normally hazardous when intrabeam exposure occurs. Viewing diffuse reflections is normally safe. Class 3B lasers may produce minor skin injuries or even ignite flammable materials
Class 4 – laser products for which intrabeam viewing and skin exposure is hazardous